## Slide 1: Cyber-Enabled Wireless Monitoring Systems for the Protection of Deteriorating National Infrastructure Systems: Distributed In-Network Computation
Mingyan Liu
Electrical Engineering and Computer Science, UM
NIST Technology Innovation Program Y1 Annual Meeting
University of Michigan, Ann Arbor, MI
July 7-8, 2010
Prospect
Solutions, LLC

## Slide 2: Computation over a network of sensors
In addition to sending raw data, can also perform in-network processing and send processed data:
  Sensor i collects a data stream xi
  Need to compute f(x1 , … xi , … xn)
  Can either have each sensor send xi to the base station (or central server), or perform the computation in-network and deliver only f()
  Pro: can potentially significantly reduce the amount of data transmitted, thereby conserve energy
  Con: may need to approximate; also need to control overhead
  Essence: feature extraction vs. data collection
Demonstrate these ideas using the example of SVD
  Optimal design of communication and computation structures
  Implementation on the Narada sensor platform

## Slide 3: In-network structural health monitoring
Singular Value Decomposition (SVD):
  Output-only modal analysis under free vibration
  One of the most common computational needs
  Generates the mode shapes of a structure

## Slide 4: Centralized vs. distributed SVD
1
2
3
4
0
5
6
F6(jω)
FFT
F5(jω)
FFT
F4(jω)
FFT
F3(jω)
FFT
F2(jω)
FFT
F1(jω)
FFT
F0(jω)
FFT
{φ1 ,φ2 ,φ3}
SVD
{φ4 ,φ5 ,φ6}
SVD
{φ0 ,φ1 ,φ4}
SVD
{φ0 ,φ1 ,φ2 ,φ3 ,φ4 ,φ5 ,φ6}
Scale and Combine
0
1
5
6
F0(jω)
F1(jω)
F5(jω)
F6(jω)
B/S
FFT
FFT
FFT
FFT
SVD
{φ0 ,φ1 ,φ2 ,φ3 ,φ4 ,φ5 ,φ6}
[Lynch et al, 2006]

## Slide 5: Optimal communication structure
Placement of operators:
  Need to determine on which nodes SVD is performed
  For each such node, determined the subset of nodes whose FFT it should collect
  Goal is to minimize the total energy consumption with possibly a computational delay constraint
Summary of results:
  Formulated as an integer linear program (ILP)
  Hardness analysis
  Without delay constraint, optimal solution given by a min. nonleaf-node data collection tree
  With delay constraint, optimal solution well approximated (with proven approx. ratio) by a degree-constrained data collection tree
  Designed distributed algorithms
5
4
6
1
2
3
0
SVD

## Slide 6: Implementation and generalization
Have implemented distributed algorithms on the Narada sensor platform:
  Automatic data collection tree construction
  Currently testing construction delay as well as stability of the tree over a network of 20 nodes
Moving forward:
  Will seek to generalize this framework:
    Functional decomposition followed by operator placement over a graph
  Tradeoff between accuracy and energy efficiency
  How to automate this process
  Other interesting examples: parallel simulated annealing
5
4
6
1
2
3
0
SVD